## Slide 1
João Vítor Correia Pessoa and D.Sc. Rafael da Silva Chaves
On Performance of Massive MIMO Systems with Solid-state Amplifiers
XLIII BRAZILIAN SYMPOSIUM ON TELECOMMUNICATIONS AND SIGNAL PROCESSING - SBrT 2025
Natal
29-09-2025

## Slide 2
INTRODUCTION
SOLID STATE AMPLIFIER MODEL
PROBLEM STATEMENT
2
01
02
03
04
05
SIMULATION RESULTS
CONTENT
MASSIVE MIMO SYSTEM MODEL
06
CONCLUSION AND FUTURE WORK

## Slide 3
3
INTRODUCTION
What is Massive MIMO?
Multiple-Input Multiple-Output technology with large antenna arrays
Base station (BS) equipped with hundreds of antennas
Benefits
Increased spectral efficiency
Improved reliability through spatial diversity
Reduced interference through beamforming
Applications
5G and beyond mobile networks
IoT and smart city infrastructure
High-density wireless deployments
Serves multiple user equipment (UE) simultaneously
Enhanced energy efficiency
Support for high-speed, low-latency communications

## Slide 4
4
PROBLEM STATEMENT
Key Hardware Challenges
Large antenna arrays increase hardware costs
Trade-off between component quality and system cost
Lower-quality hardware introduces nonlinear distortions
Degradation of spectral efficiency and channel reciprocity
Main Sources of Nonlinearity
Power Amplifiers (PAs) - Primary focus of the study
Analog-to-Digital (AD) and Digital-to-Analog (DA) converters
Impact on System Performance
Reduced energy efficiency
Impaired channel estimation accuracy
Degraded beamforming performance
High PAPR signals particularly susceptible to distortion

## Slide 5
5
PROBLEM STATEMENT
Paper Contributions
Analysis of Deterministic Physical Modeling of PAs
Uplink and Downlink Impact Analysis
Degradation Quantification
Uplink: SNR ↓ 6.5 dB (BER 10⁻⁵)
Downlink: SNR Loss < 0.3 dB (BER 10⁻³)

## Slide 6
7
MASSIVE MIMO SYSTEM DIAGRAM
Signal model for massive MIMO considering the PA nonlinearity
Downlink
Uplink

## Slide 7
SOLID STATE AMPLIFIER MODEL
8
X
Z
Nonlinearity
Ideal
Amplifier

## Slide 8
6
MASSIVE MIMO SYSTEM MODEL

## Slide 9
SIMULATION RESULTS
9
Parameter
Value
Number of antennas (M)
256
Number of UEs (K)
64, 128, 256
Constellation
500
Number of blocks
64-QAM, 256-QAM
500
Array geometry
ULA
Channel model
Rician fading
Rician factor
10 dB
BS Power
10 W
UE Power
200 mW
BS and UEs Antenna Gain
0 dBi
500
SNR range (Downlink/Uplink)
9 dB
-10 to 30 dB
Precoding/Decoding
ZF and MMSE
Monte-Carlo (UEs position)
10
Monte-Carlo (Small-scale fading)
10
Noise figure
Performance Metrics
Simulation Environment
1000-radius hexagonal single-cell system
Perfect channel state information (CSI)
Equal power allocation
Bit error Rate (BER) vs SNR
Constellation distortion analysis
SNR loss due to nonlinearity

## Slide 10
SIMULATION RESULTS – DOWNLINK
BER versus SNR for K ∈ {64, 128, 256}, A ∈ {Ideal, 1, 2}, and ZF and MMSE decoders.
ZF
MMSE
11

## Slide 11
SIMULATION RESULTS – UPLINK
11
BER versus SNR for K ∈ {64, 128, 256}, A ∈ {Ideal, 1, 2}, and ZF and MMSE decoders.
ZF
MMSE

## Slide 12
SIMULATION RESULTS
Downlink BER Performance
Downlink exhibits reduced sensitivity to PA nonlinearities compared to uplink
Power allocation and high number of antennas contribute to better resilience
Precoder Performance
ZF and MMSE precoders show similar performance in most cases
For K = 256, MMSE precoder improves performance when nonlinearity is present
System is more robust to nonlinearities in downlink than uplink
Uplink BER Performance
BER degrades with increasing number of UEs (K)
Significant sensitivity to PA saturation level
Decoder Performance
ZF and MMSE decoders perform similarly in most cases
For K = 256, MMSE decoder provides ~15.8 dB SNR gain at BER of 10
For A = 1, substantial BER degradation regardless of K and decoding algorithm
12

## Slide 13
SIMULATION RESULTS
Uplink BER versus SNR for K ∈ {64, 128, 256}, A ∈ {Ideal, 1, 2}, and ZF and MMSE decoders.
Downlink BER versus SNR for K ∈ {64, 128, 256}, A ∈ {Ideal, 1, 2}, and ZF and MMSE decoders.
ZF
MMSE
ZF
MMSE
13

## Slide 14
SIMULATION RESULTS
14

## Slide 15
SIMULATION RESULTS
15

## Slide 16
SIMULATION RESULTS
Constellation Distortion Analysis
Analysis focused on uplink decoded signal constellation
64-QAM and 256-QAM modulations evaluated at 30 dB SNR
Observed Effects
Decoded signal shows amplitude attenuation
No phase shift observed (expected with AM-AM only distortion)
Decreasing saturation level A leads to more distortion
Symbols near constellation vertices most affected
Impact on Symbol Detection
Even symbols near constellation center affected
Higher-order modulations more severely impacted
Decision boundaries compromised, increasing BER
High-Amplitude constellation points move ‘inwards’ due to gain reduction at compression
16

## Slide 17
CONCLUSION AND FUTURE WORK
Key findings
PA nonlinearities significantly degrade BER performance in massive MIMO systems
SNR losses range from 2.3 dB to 5.1 dB depending on system configuration
Future research directions
Integration of nonlinear channel estimation techniques
Design of machine learning-based precoders and decoders
Deep learning models for approximating optimal precoding strategies
Mitigation techniques for PA distortions and channel estimation errors
Uplink is more sensitive to nonlinearities than downlink
Linear signal processing often insufficient for proper signal estimation
17

## Slide 18
Power Amplifier Nonlinearities
Understanding PA Nonlinearity
Power amplifiers operate linearly only within a limited range
Beyond this range, signal distortion occurs
High Peak-to-Average Power Ratio (PAPR) signals are particularly vulnerable
Types of Distortion
AM-AM distortion:
Amplitude-to-amplitude nonlinearity
AM-PM distortion:
Amplitude-dependent phase shifts
Impact on MIMO Systems
Compromises channel reciprocity assumption
Degrades spectral efficiency
Increases bit error rate (BER)
Particularly problematic in OFDM-based systems

## Slide 19
Solid-State Amplifier Model
Nonlinearity Model Assumptions
Memoryless nonlinearities (valid for moderate bandwidths)
Focus on in-band distortion, disregarding spectral regrowth
Only AM-AM distortion considered (no phase shifts)
Solid-State Amplifier Model
f
A
(|x|) = |x| / (1 + (|x|/A)^(2p))^(1/(2p))
p > 0:
Smoothness parameter (typically 1-3)
A ∈ R
+
:
Saturation level
Higher p values → closer to ideal clipping amplifier
Lower p values → smoother transfer function
As A → ∞, PA approaches ideal amplifier
Input-Output Relationship
z = f(x) = f
A
(|x|)e^(jφ)
|x|: modulus of baseband signal
φ: phase of baseband signal
System Model
System Configuration
Single-cell massive MIMO system using TDD
Base station (BS) with M antennas
K single-antenna user equipment (UEs)
PA nonlinearity at BS (downlink) or UEs (uplink)
Downlink Model
y = √ρH
T
f(WDiag(η)
1/2
s) + v
s: transmitted signal vector
W: precoding matrix
η: power allocation vector
f(·): nonlinear PA model
Uplink Model
ỹ = √ρ̃Hf(Diag(η̃)
1/2
s̃) + ṽ
s̃: transmitted signals by UEs
η̃: uplink power allocation vector
H: uplink channel matrix